## Slide 1: Puget Sound Data Ring
Bart Kus – AE7SJ - me@bartk.us
HamWAN.org

## Slide 3
Ring Node
Distribution Node
(3-sector)
Uplink Path
Logical view of network

## Slide 5: Why?
Why do you use FM repeaters when you have a cell phone with you?
  They connect you to a different community
  In a lower pressure way
  Do not require contracts or corporations
  It’s interesting to play with their features
  They’re available when other services fail
  Those who build them love the challenge

## Slide 6: Why?
Life has advanced into the digital domain
Amateur Radio should be leading technology, not lagging! Remember the early days?
Do I really need to convey the value of all the IP-based software out there?
  Telephony
  Text messaging
  File sharing and everything else!

## Slide 7: Why?
Amateurs are in a uniquely good position to be successful at pulling this off!
  Leverage existing repeater sites
  Existing club infrastructure to rally for the cause
  Some existing financial systems to fund it
  Access to non-ISM frequencies
  Existing expertise in running radio systems
  A pool of tech-savvy early adopters / beta testers

## Slide 8: Why?
Here’s the future of radio communications, and amateurs can be on the other end of that device

## Slide 9: How?
5GHz band
  Plenty of spectrum
  Easy to achieve spatial diversity
  Low atmospheric attenuation
  Cheap and available hardware
The Puget Sound has a unique geometry
By using a ring design, coverage comes from all angles – obstacles less of a problem

## Slide 10: How?
MikroTik - Metal 5SHPn
Up to 115Mbit aggregate
Up to 1.3W transmitter
Solves hidden node problem
Only 11.5W consumption
Only $99
Serious features

## Slide 11: A Sweet Control UI

## Slide 12: A Typical Ring Node Design
Right Ring
Downlink to Distribution Node
And / Or
Sector Antenna
Left Ring

## Slide 13: A Typical Distribution Node Design
Ring Uplink
Three 120deg access sectors

## Slide 14: A Typical Client Node Design
Distribution Uplink

## Slide 15: A Typical Ring Node Cost
Description | Price | Quantity | Cost
Metal 5SHPn | $99 | 3 | $297
5GHz 28dBi Dish | $75 | 3 | $225
5-port GigE Switch | $40 | 1 | $40
Networked PDU | ~$150 | 1 | $150
CAT5 Cabling | ~$50 | 1 | $50
 |  | TOTAL | $762

## Slide 16: A Typical Distribution Node Cost
Description | Price | Quantity | Cost
Metal 5SHPn | $99 | 4 | $396
5GHz 28dBi Dish | $75 | 1 | $75
120deg Sector | $180 | 3 | $540
5-port GigE Switch | $40 | 1 | $40
Networked PDU | ~$150 | 1 | $150
CAT5 Cabling | ~$50 | 1 | $50
 |  | TOTAL | $1251

## Slide 17: A Typical Client Node Cost
Description | Price | Quantity | Cost
Metal 5SHPn | $99 | 1 | $99
5GHz 21dBi Dish | $45 | 1 | $45
CAT5 Cabling | ~$10 | 1 | $10
 |  | TOTAL | $154
Other units exist: 16dBi dish integrated with 1.25W TX for $94. Just add CAT5!

## Slide 18: 3 Node Ring + Distribution Cost
Description | Price | Quantity | Cost
Ring Node | $762 | 3 | $2286
Distribution Node | $1251 | 3 | $3753
 |  | TOTAL | $6039
That’s less than a single IC-7700 
And you get to bootstrap the future!

## Slide 20: I Want YOU To Help
Scout sites
Donate money
Raise money
Talk to your radio club
Volunteer your expertise
Help deploy equipment
Educate those new to IP